## Slide 1
FAVOR MANILA
INTERNET TEAM
Master Standard Operating Procedure (SOP)
Version 1.0 • Effective May 2026
Single Source of Truth

## Slide 2
MODULE 1
Welcome & Our Vision
OUR CORE MISSION: "We lay the cables, place the mesh nodes, watch the stream, and make sure every person — whether in the room or watching from home — experiences the service without interruption."
BEHIND THE SCENES
We do the invisible, critical infrastructure work that keeps Sundays online.
SINGLE SOURCE OF TRUTH
This deck reflects the master README.md, replacing all deprecated slides & spreadsheets.
TEAM ROSTERS & HUB
Roster details can always be checked at favor.church/techroster

## Slide 3
MODULE 1
The Volunteer Onboarding Pipeline
STEP 1: SIGN-UP FORM
Fill out the team sign-up form.
Access link from Captain or favor.church/techroster.
STEP 2: INTERVIEW
Short conversation with Captain.
Understand availability, tech comfort, and assign roles.
STEP 3: SHADOW SUNDAY
Observe a full Sunday with ZERO duties.
Get familiar with workflows, huddles, and ask questions.
STEP 4: ROSTERED SUNDAY
Active assignment with a buddy.
Own your role and follow the SOP card.

## Slide 4
MODULE 1
Roster Rules of Engagement
1. UNAVAILABILITY
Inform the Captain at least ONE WEEK in advance if you cannot make it.
Allows sufficient time to re-roster or adjust shifts.
2. COMMUNICATION
Respond to Viber GC messages within 24 hours.
Silence is not an answer. Clear communication keeps us aligned.
3. ROLE SWAPS
Arrange swaps directly with another rostered volunteer.
Inform the Captain once confirmed. Don't leave them guessing.
4. ATTENDANCE & PUNCTUALITY
Call time is 6:00 AM sharp.
Arriving late without notice is logged and hurts early setup.

## Slide 5
MODULE 1
Your First Sunday Checklist
CALL TIME
6:00 AM
SHARP
DAY 1 ACTION ITEMS
Arrive by 6:00 AM: Find the Captain at setup or text immediately.
Listen closely at the 9:00 AM Huddle: Capture venue changes or updates.
Follow your role SOP Card: Keep duty checklists open at all times.
Partner with your Buddy: Stick with your assigned experienced volunteer.
Ask Questions: No question is a dumb question on your first day.

## Slide 6
MODULE 2: TEAM ROLES & DUTIES
Setup Roles (9) and Packdown Roles (6)

## Slide 7
MODULE 2
Setup vs. Packdown Roles
SETUP ROLES (9 POSITIONS)
Captain
Operations lead and toggle execution.
Asst Captain
Floor management and field diagnostics.
Stream Op
Live feed quality and encoder monitoring.
Troubleshooting
Network support and admin panels.
Runner / Speedtester
Physical checks and node audits.
Stream Comms
Viber chat bridging (4 GCs).
Cable Hands
Lay/tape Ethernet lines (Separate from CCTV).
CCTV
Tapo camera installation.
AI Operator
Subtitles & SPF.IO setup.
PACKDOWN ROLES (6 POSITIONS)
Captain
Debrief huddle and inventory sign-off.
Cable Lead
Coils and audits all Ethernet cables (Box 1).
Cable Asst ×2
Retrieve lines from far-field nodes.
Tetris Master
Box packaging & item-by-item final audit.
AI Operator
Pack M-Audio interface and close sessions.

## Slide 8
MODULE 2
Command Center: Captain & Asst Captain
CAPTAIN (OPERATIONS OWNER)
Final Decision-Maker:
Resolves all stream, network, and team escalation points.
Timeline Responsibilities:
Toggle Restream (7 AM), runsheet huddle (8:45 AM), all-in huddle (9 AM), YT link GC (9:45 AM).
Manual Shutdown:
Turns off Resi and Restream encoders post-service.
ASST CAPTAIN (FLOOR LEAD)
Eyes & Ears on the Floor:
Manages network mesh node placements, cable runs, and client drops.
Incident Diagnostics:
Addresses slow wifi coverage zones and physical disconnects.
Critical Hand-off:
Covers floor presence so Captain can stay focused on Broadcast consoles.

## Slide 9
MODULE 2
Broadcast Console: Stream Op & Stream Comms
STREAM OP (LIVE MONITOR)
Continuous Monitoring:
Tracks Resi encoder signal, Restream dashboards, and YouTube/iWantTV quality.
Alert Rule:
Immediately alerts Captain if any destination drops or buffers.
Translations Oversight:
Monitors the AI translation subtitle feed during active windows.
*Stream Op monitors and flags; Captain executes toggles.*
STREAM COMMS (VIBER BRIDGE)
Manage Four Key Viber GCs:
1. Stream Assist Team (Ops coord) 2. Tech x Socials (Social updates) 3. iWantTV Viber (iWantTV status) 4. Kids x Tech x Babies (Ministry updates)
Key Deliverables:
Forward AJA link at 7:30 AM; forward YT link at 9:45 AM.
Backup Alerts:
Alerts all 4 GCs immediately if AJA backup is triggered.

## Slide 10
MODULE 2
Technical Support: Troubleshooting & Runner
TROUBLESHOOTING (NETWORK FIRST-RESPONDER)
Infrastructure Knowledge:
Memorizes IP schemes, router log panels, and network topology.
Setup Checks:
Verifies all routers, mesh backhauls, and switch ports are online.
Service Standby:
Monitors admin panels during service to troubleshoot network drops.
*Escalates to Captain if issue exceeds 5 minutes.*
RUNNER / SPEEDTESTER (LOGISTICS)
Physical Validation:
Carries cables and deploys mesh hardware to assigned spots.
Speedtest Checkpoints:
Speedtests every mesh node position before 9:45 AM.
Wired Rules Only:
Tests must be LAN-wired with WiFi OFF on test device (Target ≥80 Mbps).
GC Reports:
Reports all zones back to Asst Captain via Viber.

## Slide 11
MODULE 2
Infrastructure: Cables, CCTV, & AI Operator
CABLE HANDS
Route & Label Ethernet:
Switch to Broadcast, Arena PCs, and Resi Encoder.
Public Cable Safety:
Tape down runs in public pathways to prevent trip hazards.
CCTV SETUP
Tapo Camera Deploys:
Deploy Tapo C200C units at target locations.
SSID Connection:
Connect to FVR CCTV network and verify in Tapo app.
*Do not double-assign with Cable Hands!*
AI OPERATOR (TRANSLATIONS)
Hardware Connections:
Connect M-Audio USB audio interface and printer cable at MC2.
SPF.IO Settings:
Login to tech@favor.church and route audio signal correctly.
Active Toggle Windows:
Trigger AI Translations ON (~10:30 AM) and OFF (~11:30 AM) on Captain's signal.

## Slide 12
MODULE 2
Post-Service Packdown & Audits
PACKDOWN LEADER & CABLES
Captain:
Verify streams are OFF, run huddle debrief.
Cable Lead & Asst (x2):
Collect Ethernet runs, coil (over-under), store in Box 1.
AI & CCTV PACKDOWN
AI Operator:
Disconnect interface, close SPF.IO, pack gear.
CCTV:
Retrieve Tapo cameras, confirm offline in app.
THE CRTVS PACKDOWN RULE
Do NOT unplug the CRTVS table early!
They upload files post-service. Wait for Asst Captain clear.
THE TETRIS MASTER (AUDIT)
Core Responsibility:
Packs all technical equipment into designated storage boxes.
Item-by-Item Inventory Audit:
Audits packed gear against Box Inventory lists (§9).
Pre-Dismissal Sign-off:
Flags any missing items to Captain before anyone is allowed to leave.

## Slide 13
MODULE 3: SCHEDULES & PLAYBOOKS
Sunday Timeline and Step-by-Step Playbooks

## Slide 14
MODULE 3
Sunday Morning Timeline (10 AM)
Time | Event Details & Milestones | Lead Role
6:00 AM | Cable runs begin, mesh node placement, CCTV & AI setups. | All
7:00 AM | Restream ON. Set Favor Production YouTube to Unlisted. | Captain
7:30 AM | Deadline: Send AJA Restream link to STREAM ASSIST GC. | Comms
9:00 AM | All-in Internet Team huddle huddle. Run speedtest checks. | Captain/Runner
9:15 AM | iWantTV stream goes live via Oven Media Engine. | Automatic
9:45 AM | YT link to GC. Verify visibilities (FB off, iWantTV public). | Captain
9:48 AM | Resi LIVE auto-trigger. Feed live at ~9:50 AM. | Automatic
9:55 AM | Contingency Gate: Trigger AJA backup if Resi not live. | Captain
10:00 AM | Morning Service Starts. Stream Op monitors consoles. | Stream Op
12:NN | Service ends. Manually shut off Resi & Restream. | Captain

## Slide 15
MODULE 3
Early Morning Playbook (6:00 – 7:30 AM)
6:00 AM — PHYSICAL DEPLOYMENT
Huddle Gather:
Confirm full volunteer arrival. Assign buddy pairs.
Cables Deployment:
Switch to Broadcast, Arena PCs, and Resi Encoder runs.
Mesh Placements:
Asst Captain positions X50 nodes per venue layout.
Devices Check:
Launch Tapo CCTV cameras, mount AI gear at MC2.
7:00 – 7:30 AM — STREAM ACTIVATION
Toggle Restream ON (7:00 AM):
Set Favor Production YouTube destination to unlisted.
Hardware Encoders verification:
Confirm AJA Helo link light (Green) and IP in ASUS panel.
Check studio.resi.io status for Resi Encoder.
AJA Preview Link sent (7:30 AM):
Send preview link to STREAM ASSIST GC. Stream Comms verifies.

## Slide 16
MODULE 3
Mid-Morning Playbook (8:45 – 9:15 AM)
PRODUCTION HUDDLES
8:45 AM runsheet huddle:
Captain attends coordination meeting with worship and production teams. Asst Captain manages floor.
9:00 AM all-in huddle:
Full Internet Team huddles. Captain briefs team on today's stream, updates, and target assignments.
WIRED BACKHAUL AUDIT
Confirm all Deco X50 nodes show "Ethernet backhaul" (not wireless) in Deco app.
Verify Arena PCs (Propres / vMix switcher) have WiFi disabled and show link lights.
RUNNER SPEEDTEST RUN
Test all mesh locations.
Tests MUST be LAN-wired with WiFi OFF on test device.
Minimum required speed is ≥80 Mbps at every point.
Report all zone metrics back to Asst Captain via GC.

## Slide 17
MODULE 3
Live Go-Live Window (9:45 – 10:00 AM)
9:45 AM
Send YouTube link to GC. Verify final visibilities:
YT Prod = Unlisted | Backup = Unlisted | iWantTV = Public | Facebook = OFF
9:48 AM
Resi LIVE auto-trigger fires.
Stream Op verifies encoder online status in studio.resi.io dashboard.
9:50 AM
Broadcast Feed Active (2-5 min buffer delay).
Stream Op confirms visual YouTube live feed is stable with normal audio.
9:55 AM
CONTINGENCY WINDOW (Resi offline check):
If Resi is not live, Captain manually triggers AJA backup streams in Restream.
Stream Comms alerts all 4 Viber GCs immediately.

## Slide 18
MODULE 3
Afternoon Service Playbook (4 PM)
AFTERNOON TIMELINE
1:30 PM — Captain Solo Arrival:
Set YouTube unlisted. Send link to GC. Run Speedtests (target ≥80 Mbps).
2:45 PM — Runsheet Huddle:
Captain attends production runsheet huddle.
3:00 PM — Afternoon Huddle:
Gather afternoon volunteers. Verify settings.
4:00 PM — Service Starts:
Resend YT link in Viber GC during pre-roll.
6:00 PM — Post-Service:
Manual stop encoders. Post-service debrief huddle.
CORE DIFFERENCES FROM MORNING
Solo Setup Start:
Captain handles early setup checks alone. No Cable Hands or CCTV setup required (hardware stays deployed).
Speedtest Validation:
Must re-verify WAN bandwidth at 1:30 PM (ensure no congestion).
No Auto-Trigger (Resi):
Captain verifies Resi manually toggled in afternoon if schedule fails.
AI Translations:
Toggled ON (~4:30 PM) and OFF (~5:30 PM).

## Slide 19
MODULE 4: SIGNAL CHAIN & MATRIX
Stream Destinations, Signal Flow, and Metadata

## Slide 20
MODULE 4
Stream Destinations Matrix
Destination | Path | Visibility | Default State | Notes
YT-Prod TEST | Resi | — | AUTO 7:07 AM | 1-hr test; 2-5m delay
YT Production | Resi | UNLISTED | AUTO 9:48 AM | Main live stream
Facebook | Resi | — | OFF | Sundays (Disabled)
YT Backup | AJA → Restream | UNLISTED | ON 9:45 AM | 30s latency backup
YT Prod Preview | AJA → Restream | — | ON 7:30 AM | Realtime preview
iWantTV | AJA → Restream | PUBLIC | ON 9:20 AM | Oven Media relay
Facebook Backup | AJA → Restream | — | OFF | Emergency toggle only

## Slide 21
MODULE 4
Stream Signal Chain Flow
BROADCAST SWITCHER
(vMix / Tricaster Outputs)
RESI PATH (DEDICATED ISP)
1. Resi Hardware Encoder
Connects via FVR RESI (Dedicated PLDT 5G).
2. studio.resi.io Cloud
Recieves stream (2-5 min buffer delay).
3. YT Production (Unlisted)
Primary broadcast destination.
AJA/RESTREAM PATH (FVR MAIN)
1. AJA Helo Encoder
IP 10.6.33.5 via FVR MAIN (Starlink/Jireh).
2. app.restream.io Cloud
Recieves realtime stream (<30s latency).
3. Multi-Destinations:
• YT Backup (Unlisted)
• iWantTV (Public via Oven)
• FB Backup (OFF by default)

## Slide 22
MODULE 4
Stream Control Toggle Sequence
Time | Toggle Action Required | Platform | Responsible
7:00 AM | Restream ON (YT Prod unlisted) | Restream | Captain
7:30 AM | Send AJA link to GC | Viber | Captain/Comms
9:15 AM | iWantTV live (auto Oven trigger) | Oven Engine | Automatic
9:45 AM | Send YT link to GC | Viber | Captain
9:48 AM | Resi auto-trigger (LIVE) | Resi | Automatic
9:55 AM | AJA Backup if Resi not live | Restream | Captain
~10:30 AM | AI Translations ON | SPF.IO | AI Operator
~11:30 AM | AI Translations OFF | SPF.IO | AI Operator
~12:NN | Resi OFF + Restream OFF | Resi/Restream | Captain

## Slide 23
MODULE 4
YouTube Stream Metadata Setup
DESTINATION SETTINGS
Configure settings in studio.resi.io or Restream:
Title:
Join us LIVE now at Favor Church!
Category:
Nonprofit & Activism
Privacy:
Unlisted (Sundays main stream)
DESCRIPTION BLOCK (COPY-PASTE)
If you have any prayer requests, want to submit a testimony or want to know what your next step is after praying the salvation prayer, head to our website through the link in our bio!
__
📱CONNECT WITH US:
Instagram: @favor.mnl
Threads: @favor.mnl
Twitter/X: @favor_mnl
__
#favorchurch
#churchforimperfectpeople
#thefamilyyouvebeenlookingfor

## Slide 24
MODULE 5: PACKDOWN & STORAGE
Post-Service Sequence, Audits, and Box Inventory

## Slide 25
MODULE 5
Post-Service Packdown Sequence
Step 1
Terminate All Active Streams:
Stop Resi encoder in studio.resi.io. Toggle OFF Restream channels. Close SPF.IO session.
Step 2
Post-Service Huddle (5-10 mins):
Brief debrief: what went well, log issues, celebrate wins, and dismiss shadows.
Step 3
The CRTVS Packdown Rule (CRITICAL):
CRTVS table stays live post-service to upload footage. Do NOT pack power or lines there until cleared.
Step 4
Cable & Node collection:
Coil Ethernet cables (over-under) -> Box 1. Gather Deco X50 nodes (check counts) -> Box 2.

## Slide 26
MODULE 5
Equipment Audit: Box 1 & Box 2
BOX 1: CABLES INVENTORY
Item | Qty | Notes
Cat6 Ethernet (Long 20m+) | 4 | Switch to Broadcast/Arena
Cat6 Ethernet (Med 10m) | 4 | Switch to Resi/AJA/Mesh
Cat6 Ethernet (Short 3m) | 6 | Broadcast Table patch
Extension Strip | 3 | Broadcast, CRTVS, Kids
Gaffer Tape | 1 | Floor cable taping
BOX 2: NETWORKING GEAR
Item | Qty | Notes
ASUS GT-BE98 Router | 1 | Main WiFi 7 router
Deco X50 Mesh Nodes | 7 | Audit node count!
Netgear 8-Port Switch | 1 | Broadcast distribution
PLDT H153 (Jireh) | 1 | WAN 2 backup into ASUS
PLDT H153 (Resi) | 1 | Dedicated to Resi
Unicom 5G Router | 2 | UNICOM & SHILOH backup
Starlink Dish + Router | 1 | WAN 1 main source

## Slide 27
MODULE 5
Equipment Audit: Box 3, AI, & Tools
BOX 3: STREAMING GEAR
Resi Hardware Encoder (Qty: 1)
Direct connect to PLDT Resi 5G router. Handled via studio.resi.io.
AJA Helo Encoder (Qty: 1)
Fixed IP 10.6.33.5 via FVR MAIN. Handled via app.restream.io.
Tapo C200C CCTV Cameras (Qty: 2)
Main monitoring cameras. Check Tapo app configuration.
AI GEAR (TRANSLATIONS)
M-Audio USB interface (Qty: 1)
Deploys at MC2 for audio capture.
USB Printer Cable (Qty: 1)
SPF.IO audio routing connector.
TOOLS & MISCELLANEOUS
Troubleshooting Laptop (Qty: 1)
Admin panels access & speedtest verification.
Stream Comms Phone (Qty: 1)
GC Viber communication monitor.

## Slide 28
MODULE 6: VENUES & CREDENTIALS
Ynares Arena & Metrotent layouts, credentials, and rot. policy

## Slide 29
MODULE 6
Ynares Sports Arena Layout (v6)
NETWORK ARCHITECTURE RULES
Dual-WAN Failover Setup:
ASUS GT-BE98 main router accepts WAN 1 (Starlink) + WAN 2 (PLDT JIREH).
Wired Network Path:
ASUS LAN -> Netgear Switch -> AJA Helo (10.6.33.5) + Arena PCs (vMix/Propres).
Wired Mesh backhaul:
Mesh nodes must be wired to switch for backhaul (Ethernet status in Deco App).
Isolated Streaming Path:
PLDT RESI connects directly and exclusively to the Resi Encoder.
Mesh Node Placements (7):
Worship, CRTVS, Kids, Heroes, Royals, Babies, IEM.
DIAGRAM PLACEHOLDER
Double-click to insert:
1. floor-plans/ynares-v6-2026-03-03.png
2. diagrams/ynares-topology.svg
Ensure nodes layout matches locations list.

## Slide 30
MODULE 6
Metrotent Venue Layout
LEAN NETWORK RULES
WAN Configuration:
WAN 1 (Starlink) + WAN 2 (PLDT JIREH) feed into the ASUS ROG Rapture router.
Wired Distribution:
Network Switch connects AJA Helo (10.6.33.5) in the production booth.
Dedicated Stream Path:
PLDT RESI router connects directly to the Resi Hardware Encoder.
Mesh Node Placements (2):
• Node 1: CRTVS / VIP 2 area
• Node 2: Babies area
DIAGRAM PLACEHOLDER
Double-click to insert:
1. floor-plans/metrotent-v2026-01-16.png
2. diagrams/metrotent-topology.svg
Verify node placement boundaries.

## Slide 31
MODULE 6
Credentials & Security Policy
CRITICAL CREDENTIAL SECURITY RULES
No Live Passwords on Slides:
Passwords rotate periodically. Slides must NEVER hold active raw passwords to prevent breach exposures.
Authoritative Live Sources:
• Master Google Sheet: favor.church/techpasswords (link below)
• Master SOP File: README.md Section 11 in codebase
MASTER PASSWORDS GOOGLE SHEET
(Google Drive Auth Required to View)
SSID | SSID Purpose | Panel IP
FVR MAIN | ASUS GT-BE98 main router network | 10.6.33.1
FVR CCTV | Tapo C200C CCTV camera network | 10.6.33.1
FVR JIREH | PLDT H153 5G WAN 2 failover router | 10.3.1.1
FVR RESI | PLDT H153 5G dedicated Resi encoder router | 10.2.1.1

## Slide 32
MODULE 7: TROUBLESHOOTING PLAYBOOKS
Core Diagnostic Flow and Playbooks A, B, C, & D

## Slide 33
MODULE 7
Troubleshooting Principles
1. POWER
2. PHYSICAL
3. IP REACH
4. PLATFORM
5. CONTENT
BOTTOM-UP TROUBLESHOOTING RULES
Diagnose Bottom-Up:
Follow the sequence shown above. Never debug software (SPF.IO/Restream) until power and ethernet link lights show active connections.
The 60-Second Rule:
When in doubt, restart the device, wait 60 seconds, and re-test. Fixes 90% of router issues.
Verify local IP segment:
Laptop must show IP in FVR MAIN segment (10.6.33.x) to reach ASUS console.
5-Minute Escalation Limit:
If a troubleshooting volunteer cannot solve a network issue within 5 minutes, immediately escalate to the Captain.

## Slide 34
MODULE 7
Playbook A: Starlink Outage Failover
OUTAGE SYMPTOMS
No Internet access on FVR MAIN.
Speedtest registers 0 Mbps.
Deco / ASUS logs report WAN disconnection.
Starlink App displays orbital outage error alert.
STANDARD FAILOVER ACTIONS
1. Check Starlink App:
Verify system outage notice in admin logs.
2. Inspect WAN Cable:
Verify cable connection from Starlink WAN box into ASUS ROG Rapture WAN 1 port.
3. Power Cycle Starlink:
Unplug Starlink power, wait 30 seconds, replug. Wait 2 minutes for orbit locks.
4. Confirm Failover WAN 2:
Verify ASUS console (10.6.33.1) has failed over to PLDT JIREH (WAN 2 active).
5. Test LAN Speed:
Run fast.com wired to confirm bandwidth speed is ≥80 Mbps.

## Slide 35
MODULE 7
Playbook B: Encoder Streaming Failures
RESI ENCODER TROUBLESHOOTING
Symptom: YT Production shows offline after 9:50 AM.
1. Access studio.resi.io:
Verify if encoder shows 'Connected' status.
2. Check PLDT RESI (10.2.1.1):
Ensure dedicated router is online and has active LTE/5G signal.
3. Check Resi Cable:
Verify physical Ethernet between PLDT Resi LAN and Resi unit.
4. Reboot Resi unit:
Power cycle encoder. Wait 90 seconds.
*Contingency (9:55 AM):*
Trigger AJA Backup streams immediately in Restream.
AJA HELO TROUBLESHOOTING
Symptom: Restream shows no AJA source input.
1. Ping AJA Unit:
Run: `ping 10.6.33.5` from laptop.
2. Check Restream status:
Confirm AJA Helo channel is toggled ON.
3. Check AJA Input:
Verify SDI/HDMI video input cable from switcher.
4. Power Cycle AJA:
Reboot hardware encoder. Wait 60 seconds.

## Slide 36
MODULE 7
Playbooks C & D: Mesh & Slow Speeds
PLAYBOOK C: MESH OFFLINE / SLOW ZONE
Symptom: A specific venue area reports wifi dropouts.
1. Check Deco Node LED:
• [Solid Blue] = Normal • [Red/Amber/Off] = Error / Offline
2. Verify Backhaul Mode:
Check Deco App. If node is in 'Wireless backhaul', check and reseat the Ethernet cable.
3. Reboot Node:
Power cycle node. Wait 2 minutes.
4. Relocate Node:
Move closer to main router if Ethernet run is damaged.
PLAYBOOK D: SLOW SPEEDTEST (<80 MBPS)
Symptom: fast.com shows low speed during pre-service.
1. Verify wired test:
Confirm test device has WiFi OFF and is LAN-wired.
2. Check Bandwidth Hogs:
Check ASUS router client list (10.6.33.1).
Pause heavy uploads (CRTVS footage uploads) during early streams.
3. Congestion Notice:
Check Starlink app for regional satellite congestion.
4. Failover Check:
Failover streaming units to standalone 5G backup routers (Unicom/Shiloh) if LAN drops.